## Slide 1: Our script matches Fresnel at all four frequencies
Chart: |Γ| at normal incidence
| 403 MHz | 915 MHz | 2450 MHz | 5800 MHz
Fresnel, air→muscle | 0.7904 | 0.7708 | 0.7625 | 0.7567
Script, air→muscle | 0.7904 | 0.7708 | 0.7625 | 0.7567
Script, skin 1.5 / fat 8 / muscle | 0.766 | 0.651 | 0.523 | 0.867
0.7625
|Γ| air→muscle at 2.45 GHz
Fresnel error < 1e-12 (slide: 0.762, 41.9 % enters)
λ/4 match test |Γ| = 2e-16
Power balance error 7e-10
Muscle δ 22.33 mm (slide: 2.23 cm)
Surprise: the Week 1 δ fit on a 60 mm slab is off by 1.9 % even on the exact field (back-face echo).
Skipping 1.5δ at the bottom brings it to 0.4 %. Feko Model B rows go in the next version of this slide.
Notes: Reference: Fresnel with Gabriel 1996 muscle. Test 2 is a lossless quarter-wave layer (eps 3 on eps 9). The stack curve shows why the layered case matters: |Gamma| drops to 0.52 at 2.45 GHz.